## Slide 1
Qwen Transformer Block — NLPC / LPC Hardware Flow
End-to-end token flow, per-block non-linear (NLPC) vs. linear crossbar (LPC) engine split

## Slide 2
End-to-End Flow: Token → Attention → FFN → Sampling
Input prompt
Tokenization
MEM/CTRL
Embedding lookup
Hidden vector buffer
RMS Norm (NLPC)
Q/K/V projection on PE array
qnorm/knorm (NLPC)
RoPE (NLPC)
MEM/CTRL
KV cache indexing
Q * K^T PE array
Causal mask (NLPC)
softmax (NLPC)
softmax * v PE array
output projection (PE array)
Residual add 1
RMS normalization pre attention (NLPC)
Gate up projection in PE array
SiLU activation (NLPC)
SwiGLU multiply (NLPC)
Down projection in PE array
Residual add 2
LM head
Top-K
NLPC = Non-Linear Processing Core (vector ALU engine) | PE array = ReRAM crossbar linear-processing core (LPC)

## Slide 3
LPC (Linear Processing Core) — PE Internal Datapath
LPC
Input buffer
32*32 crossbar array
ADC/IV-sensing/ SAR-TDC/Wear leveling
Output buffer
Compute buffer

## Slide 4
NLPC (Non-Linear Processing Core) — Internal Datapath
NLPC
Input buffer
32*32 crossbar array
Output buffer
Compute buffer
Output buffer highlighted — staging point where NLPC results feed back into the next crossbar pass.