## Slide 1
One-Block Qwen3 Software Crossbar Hardware-Effects Audit
What happened after inference on the mapped software crossbar path
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Run Qwen3-1.7B transformer block 1 Software crossbar path, W7/A7, prefill + decode
Stimulus GPU reference prompt/tokens reused only as input No GPU comparison in this deck
Core takeaway: reliability changed stored cell levels, noise added read uncertainty, IV/ADC clipped oversized column currents, and TDC added digitization error. The largest hotspot is attention AV, especially decode.
Result folder: results/qwen3_block1_hwfx_20260623 Prompt length: 27 prefill tokens, 1 decode token

## Slide 2
Hardware Path During Inference
The hardware effects are read in the same order a crossbar would see them
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Stored weights Reliability retention + BER + state spread
Cell reads Noise thermal + shot + 1/f + RTN
Column sum IV / ADC current range + clipping
Digital readout TDC SAR-FP conversion
How to read the results: reliability is persistent storage error; noise is random read-time uncertainty; IV/ADC is analog range loss; TDC is the final analog-to-digital conversion error.

## Slide 3
Hardware Effects Summary
Measured on the software crossbar prefill + decode inference
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Reliability
5.141
mean int error max 1,217 16,831,854 INT8 entries changed
Noise
28.504
mean sigma levels max 32.352
IV / ADC
22,766
saturation events 6,680 clamped tile-columns 2,745 saturated tiles
TDC
6.664
mean int error max 58,444 22,101,664 outputs converted
Most important reading: IV/ADC and TDC show where the analog readout path is under pressure. The largest TDC hotspot is decode attention AV, with mean/max integer error 805.297 / 58,444.

## Slide 4
Reliability: What Happened To Stored Weights
ReRAM cell levels were stored, then drift/fault models were applied
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
What was modeled 30-day retention drift 0.02 log-normal state spread 10 ppm raw BER with ECC What happened 402,509,700 cell levels changed 2 raw BER flips remained 16,831,854 INT8 weight entries changed
Mean integer branch error
Prefill
4.983
Decode
9.383
Total
5.141
Interpretation Stored weights were not ideal after retention. The average branch sum moved by 5.141 integer levels; worst observed branch error was 1,217.

## Slide 5
Noise: What Happened During Each Read
Read noise is transient uncertainty, not a permanent weight change
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Noise sources included Thermal: 4 k T / R Shot: 2 q I * fano Flicker / 1/f noise RTN Readout/sense RMS noise Bandwidth integration at 5 kHz Measured uncertainty Mean sigma: 28.503848 levels Max sigma: 32.351608 levels
Mean read-noise sigma
Prefill
28.504
Decode
28.498
Total
28.504
Interpretation Every analog read has random current variation. A sigma near 28.5 levels means the same stored value can read slightly differently each time.

## Slide 6
IV / ADC: What Happened When Column Current Was Too Large
Column sums exceeded the modeled readout range and were clipped
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Readout limit Mode: hard clamp Full-scale: 2,250 product levels Row groups: 4 Observed 22,766 saturation events 6,680 clamped tile-columns 2,745 saturated tiles Max branch: 37,467
Saturation and clamped columns
Prefill events
19,411
Decode events
3,355
Prefill columns
3,463
Decode columns
3,217
Interpretation When the column current is too large, the extra analog value is lost. Clamped columns are a critical warning sign.

## Slide 7
TDC: How The Analog Result Was Converted To Digital
SAR-FP TDC adds compact readout quantization after analog limiting
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
TDC model 9-bit signed payload SAR-FP output format gain_shift = 0 Observed 22,101,664 output values converted 198,914,976 wire bits 0 extra SAR range clips Mean error: 6.663875 Max error: 58,444
Mean TDC integer error
Prefill
6.390
Decode
14.045
Total
6.664
Interpretation TDC is the final conversion from analog branch result into compact digital code. The biggest readout error appeared in decode attention AV.

## Slide 8
Prefill vs Decode Hardware Effects
Decode has fewer tokens but still large attention-context pressure
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Phase
Reliability mean/max
Noise mean/max
IV events
Clamped columns
TDC mean/max
Prefill
4.983 / 1,217
28.504 / 31.215
19,411
3,463
6.390 / 38,893
Decode
9.383 / 513
28.498 / 32.352
3,355
3,217
14.045 / 58,444
Total
5.141 / 1,217
28.504 / 32.352
22,766
6,680
6.664 / 58,444
Main reading: prefill has more total IV/ADC events because it processes 27 tokens. Decode has fewer events, but its attention context still produces high clamped-column pressure and the worst TDC error.

## Slide 9
Largest Hardware-Error Hotspots
Where the inference run is most sensitive
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Phase
Role / module
IV events
Clamped
Reliability mean
TDC mean/max
decode
attn_av / mapped_attn_av
777
747
16.569
805.297 / 58,444
prefill
attn_av / mapped_attn_av
8,834
1,628
9.917
257.360 / 38,893
decode
v_proj / v_proj
1,096
1,080
20.785
43.299 / 8,374
decode
out_proj / o_proj
540
455
14.806
19.438 / 7,452
prefill
v_proj / v_proj
1,280
420
11.035
17.505 / 7,588
Main hotspot: attention AV. Decode attention AV has the largest TDC error: mean 805.297 and max 58,444.

## Slide 10
What This Means After Inference
Hardware-only conclusion
Software crossbar hardware-effects inference audit | Qwen3-1.7B block 1
Reliability
Stored cell levels drifted; effective INT8 weights changed; branch sums moved by 5.14 levels on average.
Noise
Every read carried about 28.5 levels RMS uncertainty from analog noise sources.
IV / ADC
Some column currents exceeded range: 22,766 saturation events and 6,680 clamped tile-columns.
TDC
Final readout conversion added 6.66 mean integer error, with the worst error in decode attention AV.
Based on results/qwen3_block1_hwfx_20260623/hardware_effects_report.json